## Slide 1: Section I: Soft-bodies and Contact
Notes: Until now, the frictional contact models we have presented mostly assume the simulations involve rigid bodies. However, the same contact models and formulations are also compatible with soft-body systems. So let’s take a look at some changes that are necessary to use the LCP formulations with soft-body simulations.

## Slide 2: Soft-body Models
See related courses by Sifakis and Barbic [2012] and Kim and Eberle [2020]
Soft-bodies modeled as a mesh with nodes
  Ex. FEM tetrahedral mesh
  … but also mass-spring meshes and cloth
Undeformed positions
Generalized positions
Generalized velocities
Notes: To get started, we’ll review some of the basic of how soft bodies are modeled. And here we’ll present only the essentials that are necessary for understanding how frictional contact may be used with these models.
* For a much more in-depth treatment of soft body modeling and dynamics, we recommend the SIGGRAPH courses by Sifakis and Barbic in 2012, as well as the recent course by Kim and Eberle in 2020.
* Soft bodies in computer graphics are typically modeled as meshes with nodes. For example, tetrahedral meshes may be used to model the constitutive dynamics of elastic bodies using the Finite element method.
…. but our analysis also applies to mass-spring simulations, and even cloth.
So we’ll assume that our soft body model is a mesh that is comprised of nodes. And in the example shown, the nodes are essentially the vertices of a tetrahedral mesh,
we can write the vector of generalized positions as the concatenation of all node positions.
* And the same is true for the generalized velocities, is simply a vector containing the linear velocities of all nodes.
* Furthermore, unlike rigid bodies, which do not deform, soft-body models also keep track of the undeformed state of the mesh, and here we use the vector of vertex positions in their undeformed state. Note that the undeformed vertices aren’t so important with regards to contact, but they are important for computing elastic forces.

## Slide 3: Soft-body Constrained Dynamics
Soft body simulations use stiffness and damping to model internal elastic forces
Velocity-level dynamic equations for soft bodies:
Constraint equations:
Complementarity conditions:
Stiffness
Damping
Notes: Soft body simulations model internal elastic and dissipative forces using stiffness and damping terms in the dynamics formulation.
* This leads to a velocity-level formulation of the dynamics that looks something like the equation shown here. Note that K, the stiffness matrix and B the damping matrix appear on the left hand side of the equation, and this is important since they are being combined with the mass matrix. It is also important to note that their appearance here implies that elastic and damping forces are being computed in an implicit fashion, and implicit integration is common for many soft body simulations in order to avoid instabilities, especially for larger time step values.
* Constraint forces may also be included as part of the formulation, as shown here.
Along with the accompanying unilateral kinematic constraint equations. And we begin to see how contact models may be seamlessly integrated as part of the soft body dynamics.
And finally, the complementarity conditions for the residual velocity and contact constraint impulses may be written as we have seen before. Note that here we see the complementarity conditions in their standard form, but remember that we have seen variations of this formulation depending on the specific contact model that is being used. What is different, however, is how the contact Jacobian is assembled. We’ll still assume that the Jacobian maps generalized velocities to the contact frame, but as we have already seen the generalized velocities are different for soft body models

## Slide 4: Soft-body Contact Jacobian
Relative velocity at contact point :
Vertex-Tet Contact
6
are the barycentric coordinates of contact point
Notes: Let us consider the case of a contact between a vertex of one soft body A, and a tetrahedron from soft body B.
A contact point and normal are generated for this case. Since, from body A, only the vertex l is involved in the contact, we can say that the contact point “p” and the vertex “l” are coincident. However, from body B, it’s a bit more complicated since there’s not a single vertex involved in the contact, but rather a mesh element.
Assuming that the contact point lies on the interior or the surface of the tetrahedral element, we can express the contact point as a weighted combination of the elements vertex positions. For example, using an affine linear combination as shown here, where “w” I,j,k, and m are the barycentric coordinates of the contact point with respect to the element vertices.
Then, by write the contact point position as an expression involving the node position from each body, we have the equality that x sub l is equal to the weighted sum of positions from the vertices of body B.
This naturally leads to an expression for the relative velocity, delta v, at the contact point in terms of the nodal velocities, v, of each body. Note that again barycentric coordinates are used to interpolate the node velocities from body B.

## Slide 5: Soft-body Contact Jacobian
NCP version shown, but changes according to specific friction cone model
Only nodes involved in contact shown, but soft-bodies contain many more nodes
Global matrix is typically wide and sparse
Vertex-Tet Contact
Recall: relative velocity projected to contact space
Contact frame velocity
Notes: Recall that the contact jacobian maps the relative velocity from generalized coordinates to the velocity in the contact frame
And we can of course expand this expression and write it in matrix-vector form
Where the vector on the right are the linear velocities of all nodes involved in the contact, u
.. and the matrix term is the contact Jacobian, J
Here is shown the contact Jacobian for the non-linear friction cone model, with the first row comprising the non-interpenetration constraint, followed by the frictional constraints in the tangent and bitangent directions However, additional rows with additional tangent vectors could be added for example if we wanted to build the Jacobian for the linear polyhedral cone model
Also note that only the nodes involved in the contact are shown in this example, but typically soft body systems have many more degrees of freedom than their rigid body counterparts,
and so the global J Jacobian matrix can be quite large and sparse. Care must be taken to assemble the Jacobian to correctly index the non-zero blocks.

## Slide 6: Soft-body Constrained Dynamics
Linear system of constrained soft-body dynamics:
Compute reduced linear system may be computed by Schur complement “trick”:
Not trivial to invert, compute by e.g., sparse Cholesky factorization of
BLCP model:
Notes: The linear system for the constrained dynamics may be assembled using the Jacobian computed at each contact. More details on assembling this matrix are found in the course notes.
* Additionally, the reduced linear system that requires us to solve only for the constraint impulses may be computed by using the Schur complement “trick”, as shown here. Note that two auxiliary variables, big “W” and little “w”, are used here to simplify the expression.
Then, depending on the contact model formulation, we can apply the complementarity and feasibility conditions of the model.
* For instance, the boxed LCP conditions, as shown here. However, it’s important noting that “W”, is composed of the generalized mass matrix, damping, and stiffness matrices for the model. The mass matrix may be diagonalize, for example, by lumping mass at the nodes. However, the stiffness and damping matrices will generally not have a diagonal structure.
* And therefore “W” is not trivial to invert. Rather, the expressions involving the inverse matrix are more efficiently computed by linear solver, for instance using a sparse Cholesky factorization of “W”. Alternatively, elastic and damping forces may be computed explicitly, which would remove K and B from the lead matrix, as well as in the vector on the right hand side. However, this would likely cause stability problems for simulation of stiff materials or simulations with large time steps.